Intro to processor Architecture
Processor -report

Architectural Design:

- 2–stage pipelined processor with separate blocks for Fetch unit and the Decode and Execute unit.
- ALU implemented with 15 operations including arithmetic, logical ,shifting operations.
- Decode unit implemented with 27 instructions which gives the control signals.

Main Memory Design:

- Main memory is implemented using 2-d array in verilog.
- Main memory is a word based memory(32-bits).
- Harward type architecture is implemented with seperate memory for instructions and data
- Word length of instruction unit is 8bits.
- Word length of memory unit is 32bits.
- The size of the Main memory is declared to 2KB.
- The size of the Instruction memory is declared to 128 bytes.

Instructions Supported:

- ADD, SUB, AND ,OR, NOR, XOR, SLT, SLTU, SLL, SLLV, SRA, SRAV, SRL, SRLV,ADDI, ANDI, ORI, XORI, SLTI, SLTIU, LW, SW, BEQ, BNE, BGTZ, BLEZ ,J,greater than, less than equal .
- These are instructions given by TA on the moodle.

Instructions Not Supported:

Divsion ,Multiplication, Remainder Modulo etc.

Processor Clock Frequency:

The maximum clock frequency supported is 1.2GHz and hence the minimum clock period is 0.833ns.

Other things about the processor:

Pros:
1. 2-stage pipelined architecture.
2. Regfiles and Data memory realised using 2-D array.
3. Basic arithematic and logical programs canbe executed.
4. Loop can be implemented using branch and jump instructions.
5. Harvard architecture based memory management implemented which is ideal for embedded computer systems.
Cons:

1. Only using two stage pipeline which increases maximum clock frequency.
2. Overflow flag not raised properly.
3. Branch delay slot generated in the processorin which a NOP command should be generated.
4. Arithmetic operations like multiplication, division etc. not implemented.
5. Instructions should be pre-programmed into the memory can’t be given through test-bench.
6. Only can support word alligned read and write.

Rahul kashyap
2018102037